## Slide 1: DHT11_TempHumidity_Sens-LCD_IRremote

## Slide 2: Short description
This Arduino project measures temperature and humidity using a DHT11 sensor and displays the values on a 16x2 LCD.
Additionally, it can control an air conditioner using an IR LED driven by a 2N2222 transistor.
Components
  Arduino Mega 2560
  DHT11 temperature & humidity sensor
  LCD 16x2 with potentiometer for contrast
  IR LED + 2N2222 transistor
  Resistors and breadboard
Functions
  Read temperature and humidity data from DHT11
  Display values on LCD in real time
  Send infrared signals to control an AC (ON/OFF)

## Slide 3: Details
Purpose
  This project demonstrates the integration of sensors, display, and actuator control with Arduino.
  - Measure temperature and humidity using the DHT11 sensor.
  - Display the measured values on a 16×2 LCD screen.
  - Automatically control an air conditioner using an IR LED driven by a 2N2222 transistor.
  - Implement a simple hysteresis rule (prevents rapid switching around the threshold) :
  - If T ≥ 22 °C → AC ON
  - If T ≤ 21 °C → AC OFF
Functionality
  1. The DHT11 sensor is read every 2 seconds.
  2. Temperature and humidity values are displayed on the LCD.
  3. The Arduino checks the hysteresis condition:
  - If AC is OFF and temperature ≥ 22 °C → send IR ON command.
  - If AC is ON and temperature ≤ 21 °C → send IR OFF command.
  4. The IR LED transmits the ON/OFF commands at 38 kHz carrier frequency.
  5. The 2N2222 transistor ensures enough current flows through the IR LED for reliable range.

## Slide 6
AC on/
Klima EIN
AC off/
Klima AUS
T ≥ 22°C
T ≤ 21°C