## Slide 1: Deterministic Edge ML Architecture for Real-Time Friction Estimation (μ_used proxy based on multi-sensor vehicle data)
Sorana Mitrea

## Slide 2
Systemarchitektur (Online)
Sensoren: Multi-Modal Sensor Input Layer
IMU (a_long, ay, az, gyro) @ 100 Hz
OBD2 (v, RPM, Throttle) @ 100 Hz
(optional) Camera (Vision) @ 30 FPS
Klima (T, Humidity, p) @ 1 Hz
Zeitstempel Synchronisierung (UTC based)
Sample based Buffer: Deterministic Sample-based Data Buffer
Fixed sampling Interval (100ms)
Resampling asynchroner Sensoren
Ring Buffer Architektur
Plausibilitätschecks & Outlier Rejection
Worst-Case-Latency-Kontrolle
Feature Extraction: Real-Time Feature Engineering Layer
Ableitung von Jerk (da/dt)
RMS-Berechnung über Sliding Window
Normalisierung (Min-Max/ Z-Score)
Feature-Vektor Dimension: n=4
Laufzeit pro Zyklus: X ms
ML Model Layer: Deterministic Linear Model
Model: Ridge Regression
Feature dimension: n = 4
Training: LORO-CV (Leave-One-Run-Out)
Regularization parameter: a = 1.0
Offline validation RMSE (avg): 1.23e-4, Offline validation R2 (avg) 0.999998
Model size: ~ 10 kB ; Inference complexity: O(n)
Edge Inference: CPU based deployment
Platform: Raspbery Pi5 (ARM Cortex-A76)
Execution mode: CPU based linear inference
Fixed control cycle: 100 ms (10 Hz)
Deterministic sample based loop
Real-time μ_used estimation
μ_pred: Real-Time μ_used Estimation
Continuous μ_used prediction
Update Rate: 10 Hz
Deterministic output per control cycle
Based on longitudinal vehicle dynamics
Logging: Embedded Performance & Ressource Monitoring
Latency logging, CPU utilization, RAM usage
Temperature monitoring, Power estimation

## Slide 3
Cycle definition
    Fixed control cycle: 10 ms (10 Hz)
    Deterministic multi-sensor sampling
    Worst case latency bounded (< 10 ms)
    Closed form linear inference
Online Processing Steps (pro Zyklus)
    Sensor read (IMU, OBD2, BME, RacheChronoPro)
    Resampling & buffer update
    Feature computation (jerk, RMS, normalization)
    Linear ML inference (Ridge regression, CPU)
    μ_pred output update
    Performance logging
Deterministic Online Inference Loop
Time budget
Determinism Strategy
    Fixing 100 Hz scheduling
    Pre-allocated memory
    No dynamic model loading
    Ring-buffer based sendor handling
    Closed-form Ridge regression ensures bounded execution time
Schritt | Value*
Feature extraction | ~0.05 ms
Linear inference (CPU) | ~0.6 ms (mean)
Full cycle (worst case) | ~2.1 ms (max)
Total latency | ~2.5 ms (< 10 ms)
  *estimated for Raspberry Pi 5 (ARM Cortex-A76) using conservative 5x scaling from x86 validation measurements

## Slide 4
Hardware Awarness (current implementation)
Compute Platform
    X86 validation baseline (development platform)
    Raspbery Pi 5 (ARM Cortex-A76)
    Linux-based embedded environment
Model Design & Optimization (current implementation)
    Linear Ridge regression baseline
    Closed-forn inference (O(n))
    Regularization parameter tuning (a=1.0)
    LORO-CV (Cross-validation Leave-One-Run-Out)
    Validation under deterministic cycle constraints
Ressource Metrics
  *estimated for Raspberry Pi 5 (ARM Cortex-A76) using conservative 5x scaling from x86 validation measurements
Design Trade-offs
    Acuuracy vs latency
    Model simplicity vs interpretability
    Determinism vs adaptive scheduling
Metric | Value*
Mean interference time | ~0.6 ms
Worst case latency | ~2.1 ms
Model size | 1.33 kB
RAM footprint | ~130MB
Energy consideration
    Thermal monitoring under sustained load
    CPU Load impact analysis
    Scalability toward automotive SoC

## Slide 5
Key Architectural Contributions
Deterministic Edge AI Architecture
100 Hz fixed control loop with bounded worst-case latency
closed-form linear inference (O(n)) without dynamic graph execution
pre-allocated memory and ring-buffer based data handling
deterministic multi-sensor synchronization
Hardware Aware Deployment Strategy
cross- architecture validation (X86  ARM Cortex A76)
quantified inference latency (mean & worstcase)
explicit timing budget verification (<10 ms constraint)
ressource footprint analysis (model size, RAM usage)
Scalability Perspective
Architecture transferable to automotive-grade SoCs (CPU/NPU based architecture)
Accelerator-ready design (e.g. Coral TPU)
Separation offline optimization and deterministic runtime execution